|  | Savin Pro 8210s Console, Monochrome copier, MF Laser |
| --- | --- |
| Manufacturing Status: | New |
| Part Number: | 404930 |

| Speed Segment: 6 SRP/Street Price: $55,499/None Domestic Intro Date: November 2016 OEM: Ricoh (Japan) Also Sold As: Lanier Pro 8210s; Ricoh Pro 8210s Predecessor Model: Savin Pro 8110se Replacement Model: Replacement Date: Distribution: Dealers Max Monthly Duty Cycle: Info not avail Recommended Monthly Volume: Info not avail MULTIFUNCTION MODES Copier: Std Fax: No Internet Fax: No Network Fax: No Network Printer: Std PC Fax: No Printer: Std Scanner: Std GENERAL SPECS/PAPER HANDLING First Copy Time: 5.6 sec Multicopy (Ltr/Lgl/Ldgr): 111 cpmInfo not avail/Info not avail Warm-up Time: 360 sec Std Paper Source(s): Triple drawer Std Paper Capacity: 2,200/550/550 sheets Paper Weights: 14-lb bond to 95-lb cover Bypass/Paper Weights: Opt 550-sheet/14-lb bond to 80-lb cover Max Paper Sources/Cap: 8/12,650 sheets Max Original Size: 11 x 17 Min/Max Output Size: 3.94 x 5.5/13 x 19.2 Copy Resolution: 1200 x 4800 dpi Std/Max System Memory: 2-GB RAM, 500-GB HD/2-GB RAM, 500-GB HD Duplex: Auto (1:2.2:2,2:1) Capacity/Paper Sizes: Unlimited/5-1/2 x 8-1/2 to Info not avail Document Feeder: Std DSPF Capacity: 220 orig Paper Weights: Info not avail Sorter (Bins/Capacity): None Stapler Sorter: None Bins/Stapling Cap: Not applicable Stapling Positions: Not applicable Finisher: Opt finishers Tray/Stapling/Pos(s): 2,750, 3,250/100/4 Other: Electronic sorting; opt 550-sheet multi-bypass tray; opt 4,400-sheet LCT and 4,400-sheet vacuum-feed LCIT support paper sizes up to 13" x 19.2"/330.2 mm x 487.7 mm; opt 5,000-sheet LCT; opt SR5050 finisher has two trays (250/3,000); opt SR5060 booklet finisher has two trays (250/2,500) and V-folds up to 20 sheets (80-page booklets); opt cover interposer has two 200-sheet trays; opt multi-folding unit features Z-fold, half fold print inside and print outside, letter fold in print inside and print outside, letter fold out, double parallel print inside and print outside and gate fold print inside and print outside; opt ring binder capacity is 2 to 100 sheets and produces ring-bound books; opt Perfect Binder has maximum booklet capacity of 200 sheets (400 pages duplex); opt GBC Stream Punch; opt high capacity stakker holds 5,000 sheets - up to two can be added; opt booklet trimmer SECURITY SPECS Network User Authentication: Yes IP Address Filtering: Yes MAC Address Filtering: Info not avail HDD Overwrite: Std Max Overwrites: Info not avail HDD Encryption: Std Secure Print: Yes Encrypted Secure Print: Info not avail Encrypted PDF Mode (Encrypted Scanning): Yes IPsec: Yes Secure Sockets Layer (SSL): Yes SNMPv3: Info not avail Transport Layer Security: Info not avail Other: DataOverwriteSecurity System (DOSS) renders latent information on hard drive as unreadable; Copy Security Guard option prevents unauthorized copies; data encryption (address book, authentication password, SSL communication, S/MIME, IPsec communication, HDD); user authentication (Windows, LDAP, Basic, User Code, 802.1.x Wired), unauthorized copy/print control quota setting, SMTP over SSL; mandatory security information print (compulsory security stamp) COPIER FEATURES Automatic Features: AES, AMS, APS, AS, ASO, ATS Book Copy: Yes Job Programs: 25 Booklet Mode: Std Job Time: Yes Color: No Language: Std Copy Control: 1,000 Margin Shift: Yes Covers: Std Neg/Pos: Yes Editing: Std OHP Interleaving: Yes Energy-Save: Yes Photo Mode: Yes Erase: Std Poster Mode: No Image Insert: Yes Preset R/E: 7R, 5E Image Overlay: Std Program Ahead: Std Image Repeat: Yes Sheet Insertion: Std Image Rotate: Std Stamping: Std Interrupt: Yes Timer: Yes Job Build: Yes 2-in-1: Std XY Zoom: Yes Zoom Range: 25 to 400 (1%) OTHER FEATURES Simplified display; user tools; chapterization; copying on tabs; sample copy; stamps/numbering; Bates numbering; eco-friendly indicator; external USB keyboard support; mixed-size originals/batch mode ADDITIONAL INFORMATION Control Panel: 10.4" color touchscreen control panel monitor w/hard keys Quantity Selector: 1 to 9,999 (0 to 9 keypad) Message Display: Yes Help Key: No Dimensions (HxWxD): 57.5" x 52" x 43.3" Weight (Base Unit): 915 lbs Power Requirements: 208-240 V, 20 A Energy Used While Power Off: Info not avail Energy Used in Power Save Mode: Info not avail Energy Used in Ready Mode: Info not avail Energy Used While Copying: Info not avail Energy Used While Printing: Info not avail Energy Used While Scanning: Info not avail Max Power Consumption: 3400W TEC Value: 14KWh Dedicated Outlet: Required Energy Star Compliant: Yes Operating Noise Level: Info not avail COMMENTS Standard web browser; incorporates Ricoh's latest VCSEL technology which features a dual array of vertical cavity surface emitting lasers to produce exceptionally fine resolution at high speed; customizable full-color 10.4"/264.16 mm SVGA control panel with SD card and USB flash memory slots; Trained Customer Replaceable Units (TCRUs) can be replaced by trained users eliminating the need for a service call; standard document server holds 15,000 documents | MULTIFUNCTIONALITY Connectivity Specs Client OS Support: Win Vista, Server 2008, 7, Server 2012, 8, 8.1, 10, Mac OS X 10.5+, Citrix, Linux, Novell Netware, UNIX, SAP R/3 Parallel Interface: Opt PC Fax/Print/Scan: No/No/No Serial Interface: None PC Fax/Print/Scan: Not applicable USB Interface: Std 2.0, std 2.0 (host) x 3 PC Fax/Print/Scan: No/Info not avail/Info not avail Network Interface: Std Ethernet, opt wireless Interface Type: 10/100/1000BaseTX, 802.11a/b/g/n, Bluetooth LAN Fax/Print/Scan: No/Yes/Yes Networks Supported: NetWare: Yes Windows NT: Info not avail AppleTalk: Info not avail UNIX: Yes AS/400: Info not avail Other: Near Field Communication: No Embedded Software Platform or Extensible Solutions Interface: Embedded Software Architecture Printer Specs Engine Mfr/Model: RicohPro 8210s Compatibility: PC, Mac Speed: 111 ppm First-Page-Out Time: Info not avail Max Print Area: 12.6 x 18.9 Enhanced Resolution: Info not avail Unenhanced Resolution: 1200 x 4800 dpi Std/Max Printer Memory: Shared Controller Mfr/Model: Ricoh/Info not avail Processor/Bits/MHz: Celeron P4505/Info not avail/1.86 GHz PDL/PCL: PCL 5c/6, opt Adobe PostScript 3, opt IPDS Controller Mfr/Model: EFI/EB-34 (Fiery FS200 Pro) Processor/Bits/MHz: Intel G850/Info not avail/2.9 GHz PDL/PCL: PCL 5e/6, Adobe PostScript 3 Controller Mfr/Model: Not applicable Processor/Bits/MHz: Not applicable PDL/PCL: Not applicable Other:Send to document server; sample/locked/hold/stored/scheduled print; store and print; banner page print; PDF direct print; mail to print; classification code; Bonjour support; Windows Active Directory support; DDNS support; PCL resident font adoption; mobile driver; XPS support; WS print; media direct print; auto job promotion; poster print; WPS (Wi-Fi Protected Setup); banner printing uto to 13" x 27.5"/330.3 mm x 698.5 mm on uncoatedpaper; std/max memory for EFI EB-34 controller is 4-GB RAM/ 500-GB HDD Scanner and Image Management Specs Connection Type: Network, USB Technology/Speed: CCD/120 ipm color, 120 ipm black Max Resolution: 600 x 600 dpi TWAIN Compatible: Yes Scan Destinations: E-mail: Yes I-fax: No FTP: Yes SMB: Yes HDD: Yes URL: Yes LDAP Support: Yes File Formats Supported: JPEG, PDF, compact PDF, TIFF Scan/Image Software: Info not avail OCR Software: Info not avail File Mgmt Software: Info not avail Other:Scan to USB, SD, NCP, PDF/A, digitally signed PDF and searchable PDF; WS scanner; universal send; distributed scan management; preview before transmission; drop out color send; B&W/FC photo; B&W/FC text; auto color selection; JBIG2 compression support Facsimile Specs Scanner Technology: Not applicable Compression Method: Not applicable Modem Speed: Not applicable Max TX Resolution: Not applicable Gray Scale/Halftones: Not applicable Std/Max Fax Memory: Not applicable Min/Max Orig Size (WxL): Not applicable Max Paper/Print Width: Not applicable Correct-Order Output: Not applicable Batch Files: Not applicable Polling: Not applicable Effective Scan Width: Not applicable Battery Backup: Not applicable Relay Request: Not applicable Confid TX/RX: Not applicable Smoothing: Not applicable Dual Lines: Not applicable Timers: Not applicable Multi Access: Not applicable Transfer Hub: Not applicable Dialing Capabilities: Broadcasting (Grps/Dest): Not applicable Redial Attempts/Intervals: Not applicable One Touch/Speed Dial: Not applicable Other: Supplies/Maintenance Black drum; Yield: 2,500,000 Black toner bottle (828484); Yield: 82,000; Coverage: 6% Black developer; Yield: 860,000 Type 8200 TCRU (Set A) (404927) Type 8200 TCRU (Set B) (404948) PM Schedule: Info not avail Options TK5010 A3/DLT tray unit (404195): $1,575 Type S3 Banner tray bypass (404649) Type S3 Bypass banner sheet attachment kit (404708) BY5010 Bypass tray 550 sheets (404387): $1,470 RT5080 LCT 4,400 sheets (404537): $9,555 RT5100 LCT 4,400 sheets vacuum feed (404650): $14,052 RT5070 LCT 5,000 sheets SRA3 (404536): $5,093 500 Booklet maker Plockmatic (404715) 350 Booklet maker Plockmatic (404717) BU5010 Bridge unit (404652) Type 5010 Cart roll away for stacker (404218): $709 DU5050 Decurl unit SR5050 Finisher 3,000 sheets (404548): $6,862 SR5060 Finisher booklet (404550): $12,390 FD5020 Folding unit (404540): $10,416 GBC StreamPunch Ultra (404773) GB5010 Perfect Binder GBC (404542): $47,072 CI5030 Post sheet inserter (404539): $3,675 HCI3500 Post sheet inserter (409053) PU5020 Punch unit (404177): $1,050 RB5020 Ring Binder (404546): $26,066 SK5030 Stacker (404656): $18,654 TR5040 Trimmer (404400): $13,020 Type 1075 Bracket for card reader (411203): $164 Type B Bracket for key counter (412537): $168 FACI furniture (409061) Type 3260 Copy connect kit (412415): $1,958 EB-34 EFI Fiery controller (404926) FACI enabler (404828) Type E File format converter (414007): $817 Type M2 Interface 802.11a/g/n (416572): $800 Type A Interface Parallel (411699): $134 Type S3 Interface RPIP (404660) Type S7 Adobe PostScript 3 (404953) Type S7 IPDS unit (404954) Type G Copy Data Security Unit (416391): $960 HDD security kit for EFI print controller (404334) Type M12 Counter interface unit (417111): $81 ES-2000 Spectrophotometer ES-2000 (007095MIU): $1,295 EFI Compose (404751): $2,005 EFI ImageViewer (404827) EFI Impose (404750): $4,012 Type M2 OCR unit (416605): $340 |
| --- | --- |

INA: Information was not available from manufacturer.  NA: Not applicable.

Specs were obtained from manufacturer/distributor and not confirmed by BLI testing.

Buyers Laboratory, 80 Little Falls Road, Fairfield, NJ 07004; 973-797-2100

Reproduction illegal without written consent from Buyers Lab. [19357/United States]

©2016 Buyers Laboratory LLC